## Slide 1: Online Work Permit Steps 1: By Requester
1. Login by Initiator using Thumb Impression/ PIN
2. Message appear “ Welcome Mr………..for Online Work Permit
3. Message appear “Permit require for Cement/ Power”
Enter Deptt and section BY DROP DOWN
4. Message appear “Permit require for …….list of type of work permits appear on screen”
5. Message appear “Work details: …………………………………..to be fill by Requester”
9. Message appear “Contractor Name: …………………………………..to be fill/select from list by Requester”
10. Message appear “Co permitee Name: …………………………………..to be fill/select from list by Requester”
and verified by thumb impression
11. Permit Require Date: …………………Start Time ……………………..Expiry Time.(after point 5)
6. Message appear “Isolation Require: Yes/No to be select by Requester”
7. If “Yes” in step 6 Message appear “Select Type of Isolation Require: Type to be select by Requester from the list”
8. Message appear “Select/fill Tag number of Equipment isolation needed …….selection by Requester”
isolation list as per Section and subsection BY DROP DOWN
14. Select Custodian (Sect. Head/HOD)
12. Select Permit Precautions by the Initiator
13. Select SOP/WI for the desired work by the Initiator

## Slide 2: Online Work Permit Steps 2: Custodian (Sect. Head/HOD)
1. Notification on the Mobile of Issuer (CCR) “ Permit request raised by Mr……..waiting for your action
3. Permit Summary appear on the screen of the Issuer
4. Isolation Requirements filled by Requester checked by CCR if any additional isolation require to be mention by CCR .
2. Login by Custodian (Sect. Head/HOD) using Thumb Impression/ PIN
3. Request Approved /Rejected by Custodian with optional comment entry
Online Work Permit Steps 3: Issuer (CCR)
1. Notification on the Mobile of Custodian (Sect. Head/HOD) “ Permit request raised by Mr……..for your approval
2. Login by Issuer using Thumb Impression/ PIN
5. Isolator Name Selection by CCR.

## Slide 3: Online Work Permit Steps 4: Action by Isolator
Notification on the Mobile of Requestor pl. confirm Isolation by Isolator completed by placing Tag no. …..Lock no.
Generated against your Permit Sr. no. -----------
Isolation done Yes/No Key with me : Yes/No
2. Login by Isolator using Thumb Impression/ PIN
3. Isolation by Isolator and Generation of LOTO no. (3B) and placing of TAG along with requestor on MCC mentioning
Tag No. and Lock Number
1. Notification on the Mobile of Isolator “ Isolation request waiting for your action
Online Work Permit Steps 5: Action by Initiator

## Slide 4
Online Work Permit Steps 6: Action by CCR
3 . Following Check points filled by Issuer Flow Isolated and their control valves blinded for operational isolation and Tagged
Equipment Electrically and Mechanically Isolated and their control valves blinded for operational isolation and Tagged
Equipment Depressurized , completely emptied and cooled
Any other instruction or advise
1. Notification on the Mobile of Issuer (CCR) “ Permit No. ---- request raised by Mr……..waiting for your action
2. Login by Issuer using Thumb Impression/ PIN
3. Approved by Issuer
4. Notification on the Mobile of Initiator , Custodian and Safety officers
5. Permit details to display in CCR like flight information
3. Issuer put Isolated equipment on Local for tryout by initiator.
Online Work Permit Steps 7: Action by Initiator
1. Initiator try on local and if equipment not run Confirm Isolation to the CCR.
Online Work Permit Steps 8: Action by CCR
1. CCR remove equipments from local mode and same will confirm on the app after it permit

## Slide 5: Online Work Permit Extension Steps :
1. After validity time expiration notification to initiator Permit Having Sr. no. ------for the job is going to lost validity period.
2. If Initiator change due to shift change or any other reason then initiator change the name of initiator.
3. New initiator will review the job and extend the permit.
4. CCR will approve .
Online Work Permit Closer Steps : Initiator request for reenergize
1. Initiator will raise the request to isolator to remove Isolation “ Pl. reenergize Eqp Tag No……..Loto No. …….Lock No. …….of Permit Sr. No………….all man and Material is removed and all guards placed on the moving parts. Copy of this request to CCR(issuer) and I am giving Key to Isolator for reenergize of the equipment
Online Work Permit Closer Steps : Isolator confirmation for reenergize
1. Isolator will remove locks and Tag along with Initiator information of this action will notify on the requestor and Issuer.
Online Work Permit Closer Steps : Initiator request to close
1. Work has been completed for the permit bearing sr. no. all equipments reenergize, house keeping of the area done all guards placed and checked pl. close the permit
Online Work Permit Closer Steps : Initiator request to close
1. CCR issuer will confirm for house keeping and for guards from the concern area process engr and close the permit with Remark